## Slide 1: Automated Plant Watering System
Deepak B N 231039018
Adarsh Prabhakar 231039034

## Slide 2: Problem Statement
Develop an embedded system using a Keil development board to create an automated plant watering system. Utilize an external soil moisture sensor as an input. Implement a real-time system with processes for monitoring soil moisture levels, activating a water pump, and providing status feedback through LEDs.All these activities to be considered as periodic activities and feedback should be provided within the period.Time for the period should be as minimum as possible.

## Slide 3: Objectives
Develop an embedded system using a Keil development board to create an automated plant watering system.
Utilize an external soil moisture sensor as an input. Implement a real-time system with processes for monitoring soil moisture levels, activating a water pump, and providing status feedback through LEDs.
All these activities to be considered as periodic activities and feedback should be provided within the period. Time for the period should be as minimum as possible

## Slide 4: Hardware Components:
Keil Development Board (e.g., STM32 Discovery Board)
Soil Moisture Sensor
Water Pump
LEDs
Connecting wires

## Slide 5: Software Components:
Keil uVision IDE
Free RTOS (Real-Time Operating System)

## Slide 6: Implementation
1. Set up Hardware:
  Connect the soil moisture sensor, water pump, and LEDs to the appropriate pins on the development board.
2. Initialize FreeRTOS and Peripherals using STM32CubeMX:
  Use STM32CubeMX to generate initialization code for your microcontroller.
  Configure the necessary peripherals (GPIO, ADC, timers, etc.).

## Slide 7: Code Structure
#include "task.h"
#include "timers.h"
#include "semphr.h"
#include "stm32f4xx_hal.h"
// Task prototypes
void MoistureTask(void* pvParameters);
void PumpTask(void* pvParameters);
void LedTask(void* pvParameters);

## Slide 8
int main(void)
{
// Initialize hardware components and peripherals using STM32CubeMX-generated code // Create a mutex to protect shared resources
xMutex = xSemaphoreCreateMutex();
//Calling Functions
// Create tasks FreeRTOS scheduler
vTaskStartScheduler();
while (1) {} // Control never reaches here
}

## Slide 9: Thank You